## Slide 1: Empirical Data to Determine Transonic Drag Coefficient Land Simulation, Experimentation, and Wargaming (LSEW)
UNCLASSIFIED
Oleg Mazonka
2016

## Slide 2: Empirical Data to Determine Transonic Drag Coefficient
UNCLASSIFIED
Land Simulation, Experimentation, and Wargaming
DST Group
Land Operations Research
Army
Input Data
Detection and Identification
Behaviour
System Capabilities
Weapon – Target Interaction
Combat Simulators
Combat Simulators
Combat Simulators
Combat Simulations
Data Fidelity
Data Breadth
Traditional
V&L Modelling
Our Models
External ballistic model
Notes: Relative simplicity (input data & models)
Traceability
Fit for purpose
Common framework

## Slide 3: Empirical Data to Determine Transonic Drag Coefficient
Content
  Drag coefficient
  External ballistic model
  Drag function parametrisation
  Optimisation
UNCLASSIFIED

## Slide 4: Empirical Data to Determine Transonic Drag Coefficient
Drag coefficient
  Work produced by air friction
  Energy to accelerate air
UNCLASSIFIED
 | Drag force
 | Drag coefficient
 | Air density
 | Body cross section
 | Velocity

## Slide 5: Empirical Data to Determine Transonic Drag Coefficient
External ballistic model
  Fit-for-purpose simple to use model
    Projectile length and cross section area
    Muzzle velocity
    Supplementary ballistic data
  Included in the model
    3D trajectory
    Earth’s curvature
    Altitude: air density and temperature
  Optional
    Range and cross wind
    Air turbulence
  Not included
    6DOF; spin effects: gyroscopic, Magnus, Coriolis effects
    Non-spherical Earth
UNCLASSIFIED

## Slide 6: Empirical Data to Determine Transonic Drag Coefficient
External ballistic model
  Gravitational force
  Drag and front wind force
  Side wind force
  Air turbulence
UNCLASSIFIED
A projectile shot at 30° at 7000 ms-1 with no drag. The green line represents the earth surface.
M107 projectile shot at 30° with air turbulence parameter on. Ten trajectories are shown.

## Slide 7: Empirical Data to Determine Transonic Drag Coefficient
External ballistic model
  Gravitational force
  Drag and front wind force
  Side wind force
  Air turbulence
  G – Gravitational constant
  ME – the Earth’s mass
  RE – the Earth’s radius
UNCLASSIFIED

## Slide 8: Empirical Data to Determine Transonic Drag Coefficient
External ballistic model
  Gravitational force
  Drag and front wind force
  Side wind force
  Air turbulence
  m – mass of the projectile
  μ – Mach number
  cr – speed of sound
  ρr – air density
UNCLASSIFIED
cr – function of temperature T;
ρr – function of T, sea level pressure, molecular weight of air, universal gas constant, and free-fall acceleration constant;
T – function of sea level temperature, altitude, and temperature lapse rate

## Slide 9: Empirical Data to Determine Transonic Drag Coefficient
External ballistic model
  Gravitational force
  Drag and front wind force
  Side wind force
    assuming side drag coefficient to be 1 (side cylinder)
  Air turbulence
    Modelled as a Wiener process
    Derived from fluctuation-dissipation relation
    δ – time step of integration
    f0 – strength of turbulences (m/s)
UNCLASSIFIED
Law of cosine defines the angle at which the air hits the projectile

## Slide 10: Empirical Data to Determine Transonic Drag Coefficient
Drag function
UNCLASSIFIED

## Slide 11: Empirical Data to Determine Transonic Drag Coefficient
Drag function
μ – Mach number
α, β – some functions of μ
UNCLASSIFIED
α=0.1
β=0.3 (>1)
experimental data for M107 155mm howitzer

## Slide 12: Empirical Data to Determine Transonic Drag Coefficient
Drag function
UNCLASSIFIED
Function Cd fit to experimental data with smooth step transition function
Function Cd fit to experimental data Ball M33 Cal .5. Functions α and β are shows as well.

## Slide 13: Empirical Data to Determine Transonic Drag Coefficient
Optimisation
  Given empirical data, find trajectories corresponding to records
  Find corresponding values of calculated trajectories
  Compare the values to the original data
  Modify drag function parametrisation to improve the result
  Repeat
UNCLASSIFIED
R Angle Fall topH topR Time Vf
-----------------------------------------------------
100 - 0.0667 0.03 51 0.15 623
300 0.2333 0.3000 - 162 0.52 -
500 - 0.8000 1.3 - 1.04 334
600 - 1.1500 2.3 344 1.35 304
800 1.1000 2.1000 5.5 468 2.05 266
V Max
------------
207.3 3900
234.7 4800
268.2 6100
310.9 7800
371.9 9700

## Slide 14: Empirical Data to Determine Transonic Drag Coefficient
Optimisation
  [Cd] – parameters of Cd o
  x – input data
  y – calculated values
UNCLASSIFIED
R Angle Fall topH topR Time Vf
-----------------------------------------------------
100 - 0.0667 0.03 51 0.15 623
300 0.2333 0.3000 - 162 0.52 -
500 - 0.8000 1.3 - 1.04 334
600 - 1.1500 2.3 344 1.35 304
800 1.1000 2.1000 5.5 468 2.05 266
V Max
------------
207.3 3900
234.7 4800
268.2 6100
310.9 7800
371.9 9700
R Angle Fall topH topR Time Vf
-----------------------------------------------------
100 0.0833 0.0667 0.03 51 0.15 623
300 0.2333 0.3000 0.34 162 0.52 459
500 0.4833 0.8000 1.3 282 1.04 334
600 0.6667 1.1500 2.3 344 1.35 304
800 1.1000 2.1000 5.5 468 2.05 266
V Max
------------
207.3 3900
234.7 4800
268.2 6100
310.9 7800
371.9 9700

## Slide 15: Empirical Data to Determine Transonic Drag Coefficient
Summary and conclusion
  External ballistic model uses fit-for-purpose easy to use approach without sacrificing fidelity hidden from the user
  Drag function is parametrised by splitting into two components
  Global optimisation is used to match empirical ballistic data by modifying the drag function
  The code is written in C++, is open source (Github)
    Global optimisation is done over the utility function U which is the result of other optimisation algorithms – U is not smooth because of computational noise
    Computational tricks making trajectory integration fast
UNCLASSIFIED